## Slide 2: Development of A Parametric Tool for Automated Slot Insulation Insertion in Small-Scale Electric- Motor Stator Production
Alen Sebastian 23221507 (M Sc Electromobility)
Project Thesis Presentation

## Slide 3: Workflow and Key Components of Developing a Parametric Tool for Slot Liner Insertion:
Motivation
Objectives
Key steps involved in motor manufacture
Slot-Liner Function and Importance
Insertion of Slot Liners in Large Scale Manufacture
Insertion of Slot Liners in Small Scale manufacture
Proposed Automation Plan
Hardware Setup
Parametric Tool Development
Initial Design vs Final Design
Testing and Validation
Conclusion and Outlook

## Slide 4: Climate change and CO₂ emissions drive the need for sustainable mobility, leading to a rapid rise in electric vehicle demand.
Climate change & CO₂ emissions  need for sustainable technologies
Transport sector accounts for about 23% of global CO2 emissions
Electrification trend  rapid growth of EVs surge in electric motor demand
Large-scale production: highly automated
Small-scale/custom production: still manual, especially slot liner insertion
Manual process = time-consuming, inconsistent, costly
Global EV sales [1]

## Slide 5: Objective: To Develop a flexible insertion tool to automate slot-liner insertion in small-scale stator manufacturing
Automated Slot-Liner Insertion
Parametric Tool Design
Flexible manufacturing
Robotic Integration and validation
Process reliability and repeatability

## Slide 6: Producing a stator requires a sequence of precise manufacturing steps, ensuring structural integrity, insulation, and electrical reliability.
Key steps in stator manufacture involve:
Core Preparation – Laminated electrical steel sheets are cut, stacked, and bonded to form the stator core.
Insulation Insertion – Slot liners and other insulation elements are placed to isolate windings from the core.
Winding & Interconnection – Copper wires are wound into slots and interconnected (crimping, soldering, welding).
Stabilization & Testing – Resin impregnation improves insulation and thermal performance, followed by electrical tests for quality assurance.
Fully assembled motor [2]

## Slide 7: Why Slot liners are Important in Stator Manufacture:
Winding Retention
Electrical Insulation
Thermal Management
Wear Resistance
Slot Insulation in a stator [3]

## Slide 8: How slot liners are inserted in large scale manufacture such as in the automotive industry:
Large batch manufacture with constant motor size.
High speed insertion (3 sleeves per second).
Integrated cutting, folding and creasing.
Not suitable for high variance, low volume production.
High Investment costs.
. GMW CS-5E Horizontal Slot Cell Inserter [4]

## Slide 9: How slot liners are inserted in small scale manufacture such as in aviation or naval industries:
High variance low volume production.
Insertion is done manually.
Use of jigs, cutting/folding machines.
Labor intensive, difficult to scale.
Flexible, low cost.
*AI generated image
manual insertion of slot liner

## Slide 10: Proposed Automation Plan
Goal: Automate slot liner insertion for small-scale, high-variant motor production.
Approach:
Develop a parametric tool adaptable to different stator sizes and shapes.
Integrate with a collaborative robot setup (UR10e, gripper, FT sensor).
Workflow Concept:
Slot liner positioning
Orientation with funnel/clamp system
Automated insertion with robotic guidance
Expected Benefits:
Increased precision and repeatability
Reduced labor intensity and errors
Flexibility for small-batch, high-variance manufacturing
Automated insertion of slot liner

## Slide 11: Robotic Module for Automated Insertion: UR10e Collaborative Robot, RG2 Gripper, and Force/Torque Sensor
UR10e Cobot:
Provides precise programmable motion 12.5 kg payload 1300 mm reach compact and safe Easily adaptable for flexible manufacturing
RG2 Gripper:
Adjustable 2 finger gripper 110 mm stroke length Intelligent grip detection Customizable fingertips Suitable for secure handling of Slot Liners
HEX Force-Torque Sensor:
Real-time force monitoring 6 axis Force Torque measurement Ensures accurate insertion of liner Misalignment detection Configurable force thresholds
Source: UR robots [5]

## Slide 12: Mechanical Fixtures for Accurate Positioning of Stator, Slot Liner, and Funnel
Rotating Mechanical Clamp
Rotating Mechanical Clamp
Slot Liner and Funnel Positioning Platforms
1). User-defined rotation aligns each slot with the funnel for fully automatic insertions. 2). Servo Motor + Siemens S7-1500 PLC - Provides precise, deterministic low-level motion control. 3). Manual origin calibration, stop-rotation function for safety, collision avoidance, and adaptability
1). Secure, repeatable positioning for insertion tool and slot liners 2). Quickly accommodates different stator or slot liner geometries with minimal downtime. 3). Ensures accurate robot grasping, reducing misalignment and improving repeatability. 4). Enhances workflow efficiency in small-batch or high-mix production while maintaining precision.

## Slide 13: Key Parameters Considered for the Parametric Funnel Development:
Slot Width
Slot Height
Slot Angle
a) tool parameters
b) Actual slot in a stator

## Slide 14: Initial Funnel Design: Parametric Geometry and Guiding Mechanism for Slot Liner Insertion.
a) Front view
b) Rear view
c) Side view
d) Top view
Parametric funnel geometry, adaptable for different slot sizes.
Inner and outer guide rails to maintain precise alignment with the stator slot.
Cheap and Easily prototyped. Material used - PLA
Flared, tapered internal channel, that guides the slot liner smoothly towards the stator slot.

## Slide 15: Observations and Limitations of the Initial prototype.
Initial Prototype
Final Prototype
Prototype Evaluation:
The initial prototype confirmed the feasibility of the parametric funnel concept but revealed key weaknesses
Three external guide rails made insertion process-sensitive and dependent on precise alignment.
Short tail section and wide inlet shifted the center of gravity forward, causing funnel instability
Complex geometry reduced adaptability across stator types
Findings guided redesign for improved tolerance, locking, and stability in automated use.

## Slide 16: Final Design Development: Addressing the Shortcomings of the Initial Funnel Design
a) Front view
b) Rear view
c) Top view
d) Side view
e) Isometric view
Simplified guiding system: Replaced three rails with a single elongated rail featuring grooves for mechanical locking and easier insertion.
Improved stability: Extended and thickened tail (by 50 mm) to shift the center of gravity rearward and prevent forward tilting.
Refined outlet geometry: Slightly undersized outlet (2–3%) ensures smooth liner entry without edge damage.
Enhanced adaptability: Simplified overall geometry for easier parametric adjustments and faster design modifications.

## Slide 17: Insertion Pipeline: Complete Automation of Stator Slot Insulation.

## Slide 18: Funnel Validation: Evaluation Using Stators of Differing Geometries
Stator A
Slot Height – 20 mm
Slot Width – 8 mm
Slot angle – 85 deg
Stator B
Slot Height – 22 mm
Slot Width – 8 mm
Slot angle – 85 deg
Stator C
Slot Height – 18 mm
Slot Width – 5 mm
Slot angle – 89 deg
Slot Height – 19.8 mm
Slot Width – 8 mm
Slot angle – 85 deg
Funnel A
Slot Height – 21.80 mm
Slot Width – 8 mm
Slot angle – 85 deg
Funnel B
Slot Height – 17.80 mm
Slot Width – 5 mm
Slot angle – 89 deg
Funnel C

## Slide 19: Performance Evaluation: Testing Results for All Three Stator Geometries.
Chart: Preliminary Trials - Success Rate
| Stator A | Stator B | Stator C (N/A)
 | 0.8 | 0.7 | 0
Chart: Optimized Trials - Success Rate
| Stator A | Stator B | Stator C
 | 0.97 | 0.97 | 1
260 insertion trials were conducted across three stators (A:100, B:100, C:60) to evaluate reliability and repeatability.
Preliminary trials for Stators A & B identified issues and refined parameters; Stator C tested directly with optimized settings.
Detailed records of defects and failure modes provided critical data for further system improvement.
The parametric insertion setup delivers consistent, repeatable, and robust liner placement, achieving a 97% success rate for Stators A and B, and 100% for Stator C

## Slide 20: Error Analysis: Comparative Observations for the Three Stator Geometries.
Chart: Stator A - Preliminary Trials
| Slot liner pulled back with the funnel | Slot liner misplacement
 | 0.75 | 0.25
Chart: Stator B - Preliminary Trials
| Poor Slot liner profile | Funnel Misalignment
 | 0.9 | 0.1
Stator A: 8 errors observed (6 pull-back with funnel, 2 misplacement on platform); improvements included standardized gripper handling, deeper insertion with inner finger, and stepwise funnel retraction, raising success rate from 80% to 97%.
Stator B: 10 errors observed (9 improper insertion, 1 funnel misalignment); improvements included controlled folding for consistent liner profiles and optimized funnel/gripper handling, increasing success rate from 77% to 97%.
Stator C: No errors observed in 60 trials; process performed flawlessly using optimizations from A & B, achieving 100% success even with the most constrained slot geometry.

## Slide 21: Discussion of Results: Insights and Areas for Further Improvement
Success rates & cycle time: Optimized trials achieved 96.7% for Stators A & B and 100% for Stator C; average cycle time ~39.8 s, with room for improvement via motion optimization.
Process sensitivity: Performance depends heavily on slot liner geometry and consistency; small deviations can cause errors.
Current limitations: The process does not yet incorporate automated folding, creasing, or shaping of liners.
Potential improvements: Automating liner pre-processing and integrating pre-positioned dispensers can reduce variability, minimize robot travel, and improve cycle time
Industrial relevance: Adding vision-based quality assurance and adaptive feedback could enable a fully autonomous, scalable, flexible, and robust solution for stator assembly

## Slide 22: References
[1] IEA (2025), Global electric car sales, 2014-2024, IEA, Paris. https://www.iea.org/data-and-statistics/charts/global-electric-car-sales-2014-2024, Licence: CC BY 4.0
[2] Tiismus, Hans & Kallaste, Ants & Naseer, Muhammad & Vaimann, Toomas & Rassõlkin, Anton. (2022). Design and Performance of Laser Additively Manufactured Core Induction Motor. IEEE Access. 10. 1-16. 10.1109/ACCESS.2022.3173317.
[3} Nguyen, M. , Dario, S. , Malec, D. , Mary, D. , Cambronne, J. , Prunel, D. and Orgelet, J. (2017) Environmental Assessment and Dielectric Performances of the Secondary Electrical Insulation in Low Voltage Motors Impregnated by Different Techniques. Engineering, 9, 860-873. doi:10.4236/eng.2017.910051
[4] GMW Taiwan, GMW CS-2B Stator Slot Cell Inserter. [Online]. Available: https://​www.gmwtaiwan.com​/​Slot-​Cell-​Insertion-​Machine/​GMW-​CS-​2B-​Stator-​Slot-​Cell-​Inserter

## Slide 24
Questions?