## Slide 2: Development of A Parametric Tool for Automated Slot Insulation Insertion in Small-Scale Electric- Motor Stator Production
Alen Sebastian 23221507 (M Sc Electromobility)
Project Thesis Presentation

## Slide 3: Table of Contents
Motivation and objectives
Fundamentals of Electric Motor Manufacture
Slot-Liner Function and Importance
Insertion of Slot Liners in Large Scale Manufacture
Insertion of Slot Liners in Small Scale manufacture
Proposed Automation Plan
Hardware Setup
Parametric Tool Development
Insertion Pipeline
Testing and Validation
Conclusion and Outlook

## Slide 4: Motivation: Climate Change and Increase in demand for EVs.
Climate change & CO₂ emissions  need for sustainable technologies
Transport sector accounts for about 23% of global CO2 emissions
Electrification trend  rapid growth of EVs surge in electric motor demand
Large-scale production: highly automated
Small-scale/custom production: still manual, especially slot liner insertion
Manual process = time-consuming, inconsistent, costly
Fig 1: Global EV sales [1]

## Slide 5: Objective: To Develop a flexible insertion tool to automate slot-liner insertion in small-scale stator manufacturing
Automated Slot-Liner Insertion
Parametric Tool Design
Flexible manufacturing
Robotic Integration and validation
Process reliability and repeatability

## Slide 6: Key Steps Involved in the Manufacture of a Stator:
Core Preparation – Laminated electrical steel sheets are cut, stacked, and bonded to form the stator core.
Insulation Insertion – Slot liners and other insulation elements are placed to isolate windings from the core.
Winding & Interconnection – Copper wires are wound into slots and interconnected (crimping, soldering, welding).
Stabilization & Testing – Resin impregnation improves insulation and thermal performance, followed by electrical tests for quality assurance.

## Slide 7: The Entire Stator Assembly Process from Insulation to Winding:

## Slide 8: Why Slot liners are Important in Stator Manufacture:
Winding Retention
Electrical Insulation
Thermal Management
Wear Resistance

## Slide 9: How slot liners are inserted in large scale manufacture such as in the automotive industry:
Large batch manufacture with constant motor size.
High speed insertion (3 sleeves per second).
Integrated cutting, folding and creasing.
Not suitable for high variance, low volume production.
High Investment costs.

## Slide 10: How slot liners are inserted in small scale manufacture such as in aviation or naval industries:
High variance low volume production.
Insertion is done manually.
Use of jigs, cutting/folding machines.
Labor intensive, difficult to scale.
Flexible, low cost.

## Slide 11: Proposed Automation Plan
Goal: Automate slot liner insertion for small-scale, high-variant motor production.
Approach:
Develop a parametric tool adaptable to different stator sizes and shapes.
Integrate with a collaborative robot setup (UR10e, gripper, FT sensor).
Workflow Concept:
Slot liner positioning
Orientation with funnel/clamp system
Automated insertion with robotic guidance
Expected Benefits:
Increased precision and repeatability
Reduced labor intensity and errors
Flexibility for small-batch, high-variance manufacturing

## Slide 12: Robotic Module for Automated Insertion: UR10e Collaborative Robot, RG2 Gripper, and Force/Torque Sensor
UR10e Cobot:
Provides precise programmable motion 12.5 kg payload 1300 mm reach compact and safe Easily adaptable for flexible manufacturing
RG2 Gripper:
Adjustable 2 finger gripper 110 mm stroke length Intelligent grip detection Customizable fingertips Suitable for secure handling of Slot Liners
HEX Force-Torque Sensor:
Real-time force monitoring 6 axis Force Torque measurement Ensures accurate insertion of liner Misalignment detection Configurable force thresholds

## Slide 13: Mechanical Fixtures for Accurate Positioning of Stator, Slot Liner, and Funnel
Rotating Mechanical Clamp
Rotating Mechanical Clamp
Slot Liner and Funnel Positioning Platforms
1). User-defined rotation aligns each slot with the funnel for fully automatic insertions. 2). Servo Motor + Siemens S7-1500 PLC - Provides precise, deterministic low-level motion control. 3). Manual origin calibration, stop-rotation function for safety, collision avoidance, and adaptability
1). Secure, repeatable positioning for insertion tool and slot liners 2). Quickly accommodates different stator or slot liner geometries with minimal downtime. 3). Ensures accurate robot grasping, reducing misalignment and improving repeatability. 4). Enhances workflow efficiency in small-batch or high-mix production while maintaining precision.

## Slide 14: Parametric Tool Development
Design Considerations
Slot Width
Slot Height
Slot Angle

## Slide 15: Initial Design
a) Front view
b) Rear view
c) Side view
d) Top view
Parametric tool geometry easily adaptable for different slot sizes.
Inner and outer guide rails to maintain precise alignment with the stator slot.
Cheap and Easily prototyped. Material used - PLA
Flared, tapered internal channel, that guides the slot liner smoothly towards the stator slot.

## Slide 16: Observations and Limitations of the Initial prototype
Initial Prototype
Final Prototype
Prototype Evaluation:
The initial prototype confirmed the feasibility of the parametric funnel concept but revealed key weaknesses
Three external guide rails made insertion process-sensitive and dependent on precise alignment.
Short tail section and wide inlet shifted the center of gravity forward, causing funnel instability
Complex geometry reduced adaptability across stator types
Findings guided redesign for improved tolerance, locking, and stability in automated use.

## Slide 17: Final Design
a) Front view
b) Rear view
c) Top view
d) Side view
e) Isometric view
Simplified guiding system: Replaced three rails with a single elongated rail featuring grooves for mechanical locking and easier insertion.
Improved stability: Extended and thickened tail (by 50 mm) to shift the center of gravity rearward and prevent forward tilting.
Refined outlet geometry: Slightly undersized outlet (2–3%) ensures smooth liner entry without edge damage.
Enhanced adaptability: Simplified overall geometry for easier parametric adjustments and faster design modifications.

## Slide 18: Insertion Pipeline

## Slide 19: Validation
Stator A
Stator B
Stator C
Slot Height – 20 mm
Slot Width – 8 mm
Slot angle – 85 deg
Slot Height – 22 mm
Slot Width – 8 mm
Slot angle – 85 deg
Slot Height – 18 mm
Slot Width – 5 mm
Slot angle – 89 deg

## Slide 20: Testing Results
Chart: Preliminary Trials - Success Rate
| Stator A | Stator B | Stator C (N/A)
 | 0.8 | 0.7 | 0
Chart: Optimized Trials - Success Rate
| Stator A | Stator B | Stator C
 | 0.97 | 0.97 | 1

## Slide 21: Error Rates
Chart: Stator A - Preliminary Trials
| Slot liner pulled back with the funnel | Slot liner misplacement
 | 0.75 | 0.25
Chart: Stator B - Preliminary Trials
| Poor Slot liner profile | Funnel Misalignment
 | 0.9 | 0.1

## Slide 22
[1] IEA (2025), Global electric car sales, 2014-2024, IEA, Paris
https://www.iea.org/data-and-statistics/charts/global-electric-car-sales-2014-2024, Licence: CC BY 4.0
Joining of the Laminated Electrical Steels in Motor Manufacturing: A Review

## Slide 24: Linien etc
1
Projektvergleich starten
Projektvergleich starten
1
2
3
4
5
wicklungstyp = 1
1 A bei 50 Hz
1 A bei 50 Hz
1
3,55
3,65
16,3
4,4
Leistungsteil Induktionsanlage
Kühleinheit Induktionsanlage
Gegenwerkzeug zur Fixierung und Ausrichtung der Einzelbleche
Trägermaterial (Kupfer)
B
D
Außenmaß
Leitermaß
Anvil
Anvil
Switch on/off control voltage